## Slide 1: Cross Synthesis Using MATLAB
BY : Shabarish Kumar. R
Sankara Subramanian. M
Naveen. N

## Slide 2: What is cross synthesis?
A technology of impressing the spectral envelope of one sound on the flattened spectrum of another sound.
Used as musical instruments consist of a keyboard synthesizer (for playing the carrier sounds) and a microphone for picking up the voice of the performer (to extract the modulation envelope).
Examples : creating a talking organ or talking wind.

## Slide 3: Sound signal requirement :
The basic necessities to perform cross synthesis are two sounds.
A modulator sound .
And a carrier sound.
The sound signal such as the voice, which is to be impressed is called the modulator.
The sound signal which is to be flattened to provide the base for the modulator is called the carrier sound.

## Slide 4: Summarising the steps involved :
Performing Short-time fourier transform on both the carrier and modulator waves.
Extracting the spectral envelope of each time frame of the modulator and the carrier waves.
Dividing the spectrum of each time frame of the carrier wave by its own carrier, thereby flattening it.
Multiplying the flattened spectrum of the carrier with the envelope of the modulator, thereby replacing the envelope of the carrier.

## Slide 5: Short- time Fourier Transform
Is a powerful general-purpose tool for audio signal processing.
Defines a particularly useful class of time-frequency distributions which specify complex amplitude versus time and frequency for any signal.
Measuring model parameters in a short-time spectrum.

## Slide 6: Why prefer STFT over DFT
The major advantage of preferring STFT over DFT is that, by taking the STFT of the audio signal, we can get the spectrum of the signal for each little time frame.
Dividing the signal into small time frames and replacing the spectral envelope of that particular time frame of the carrier by that of the modulator, in turn increases the clarity of the output signal.

## Slide 7: Spectral Envelope
A spectral envelope is a curve in the frequency-amplitude plane, derived from a Fourier magnitude spectrum.
It describes one point in time (one window, to be precise).
Regarding Cross synthesis, Spectral envelope extraction is done by Cepstral smoothening method.

## Slide 8: Cepstral smoothening.
The spectral envelope obtained by cepstral windowing is defined as
where w is a lowpass-window in the cepstral domain. A simple but commonly used lowpass-window is given by

## Slide 9: Spectral Envelope by Cepstral smoothening
Perform the inverse FFT to obtain the real cepstrum, lowpass-window the cepstrum, and perform the FFT to obtain the smoothed log-magnitude spectrum.
Then window the log magnitude spectrum using the hanning window to get the smoothened spectrum which consisits of only the real part and normalize it to zero mean.

## Slide 10: Cross synthesized sound
If all the procedure above have been performed correctly we will be able to get a cross-synthesized sound which is modulated carrier as shown below